## Slide 1: FX.25 KISS TNC development and Proposed extensions to the standard
Packet Radio Users’ Group
Sep.03, 2020
Kazuhisa Yokota, JN1DFF
Masaaki Yonezawa, JE1WAZ
Norito Nemoto, JH1FBM
Notes: Packet Radio Users’ Group

## Slide 2: FX.25 KISS TNC development and Proposed extensions to the standard
Packet Radio Users’ Group
Sep.03, 2020
Kazuhisa Yokota, JN1DFF
Masaaki Yonezawa, JE1WAZ
Norito Nemoto, JH1FBM
Notes: This presentation will describe the features and configuration of the FX.25 compatible TNC currently under development.
It will also include proposed enhancements to the FX.25 standard.

## Slide 3
PRUG is a non-profit, voluntary organization in Japan.
It was established in 1985.
The purpose of PRUG is to promote the use of packet radio and to research the latest technologies in amateur radio.
PRUG (Packet Radio Users' Group)
Notes: PRUG (Packet Radio Users' Group) is a non-profit, voluntary organization in Japan.
It was established in 1985.

## Slide 4: Current status of FX.25 KISS TNC development
Notes: This section describes the development status of the FX.25 KISS TNC.

## Slide 5
FX.25
TNC
AX.25
TNC
reliable communication
with error correction
between FX.25 station
and AX.25 station
compatible with current system
FX.25
TNC
TRX
Wi-Fi
installation flexibility
using Wi-Fi interface
FX.25
TNC
TRX
independent sensor node
sensors
I2C
future plan
FX.25
TNC
TRX
USB
MIC
SP
PTT
between FX.25 stations
PC
TRX
TRX
PC
Use of FX.25 KISS TNC
and future plan
Now experimenting in the
430MHz band as APRS nodes.
Look for JK1MLY
Notes: The FX.25 KISS TNC is in the alpha test phase.
It is operating as an APRS node at 430 MHz and has proven to be compatible with AX.25 stations.
Currently it uses UI-VIEW as an application.
Look for JK1MLY on APRS network.
It's running FX.25 station.

## Slide 6
FX.25
TNC
AX.25
TNC
reliable communication
with error correction
between FX.25 station
and AX.25 station
compatible with current system
FX.25
TNC
TRX
Wi-Fi
installation flexibility
using Wi-Fi interface
FX.25
TNC
TRX
independent sensor node
sensors
I2C
future plan
FX.25
TNC
TRX
USB
MIC
SP
PTT
between FX.25 stations
PC
TRX
TRX
PC
Use of FX.25 KISS TNC
and future plan
Now experimenting in the
430MHz band as APRS nodes.
Look for JK1MLY
Notes: There is a plan to add Wi-Fi to interface with the PC.
The goal is to increase the flexibility of the TNC's Installation location.

## Slide 7
FX.25
TNC
AX.25
TNC
reliable communication
with error correction
between FX.25 station
and AX.25 station
compatible with current system
FX.25
TNC
TRX
Wi-Fi
installation flexibility
using Wi-Fi interface
FX.25
TNC
TRX
independent sensor node
sensors
I2C
future plan
FX.25
TNC
TRX
USB
MIC
SP
PTT
between FX.25 stations
PC
TRX
TRX
PC
Use of FX.25 KISS TNC
and future plan
Now experimenting in the
430MHz band as APRS nodes.
Look for JK1MLY
Notes: There is another plan to run applications within the TNC.
This is intended to realize a independent sensor node.

## Slide 8: Features of FX.25 KISS TNC
Using TI TCM3105 Bell 202 modem chip
  Implements software modem on next version
Using ESP-WROOM-32 Wi-Fi module
  Dual core 32bit RISC CPU, clock 80-240MHz
  RAM 520kB, flash ROM 4MB
Host interface is USB serial and TCP/IP on Wi-Fi
KISS mode only
supports full FX.25 draft spec.
  http://www.stensat.org/docs/FX-25_01_06.pdf
can receive AX.25 packet, too
Notes: We use a BELL 202 compatible TCM3105 modem chip.
This is because of the importance of physical layer compatibility.
We plan to implement a software modem in the next version.

## Slide 9: Features of FX.25 KISS TNC
Using TI TCM3105 Bell 202 modem chip
  Implements software modem on next version
Using ESP-WROOM-32 Wi-Fi module
  Dual core 32bit RISC CPU, clock 80-240MHz
  RAM 520kB, flash ROM 4MB
Host interface is USB serial and TCP/IP on Wi-Fi
KISS mode only
supports full FX.25 draft spec.
  http://www.stensat.org/docs/FX-25_01_06.pdf
can receive AX.25 packet, too
Notes: The ESP-WROOM-32 Wi-Fi module is the key component.
It can handle multiple channels of error correction and software modems due to the high processing power of the CPU.

## Slide 10: Features of FX.25 KISS TNC
Using TI TCM3105 Bell 202 modem chip
  Implements software modem on next version
Using ESP-WROOM-32 Wi-Fi module
  Dual core 32bit RISC CPU, clock 80-240MHz
  RAM 520kB, flash ROM 4MB
Host interface is USB serial and TCP/IP on Wi-Fi
KISS mode only
supports full FX.25 draft spec.
  http://www.stensat.org/docs/FX-25_01_06.pdf
can receive AX.25 packet, too
Notes: The power supply is also provided by USB when interfaced to the host.

## Slide 11: FX.25 KISS TNC hardware
TCM3105
Wi-Fi
module
RXD
CDT
TXD
TXA
RXA
PTT
SP
MIC
GPIO
GPIO
GPIO
GPIO
PC
USB
TX
RX
USB
Serial
Bell 202
Pulse(TTL)
UART
(TTL)
FX.25 KISS TNC
Radio
Notes: The hardware configuration is very simple.
The next version will use a software modem and will not require the TCM3105 modem chip.

## Slide 12: Structure of TNC software
Implemented by C language
Running on FreeRTOS
Each functions implemented as tasks of OS
Using queues inter task communication
Using interrupt to read RXD signal of modem
Using infra red I/F to send the data to modem
Implements software modem on next version
  The TNC software is available on GitHub
    https://github.com/amedes/fx25-kiss-tnc
Notes: The software is written in C language.
FreeRTOS is used.
Each function is defined as a task in the OS.
This makes the software more readable and easier to modify.
The software is available on GitHub.

## Slide 13: Proposed extensions to the Fx.25 standard
Notes: This chapter proposes an extension to the FX.25 standard.

## Slide 14: Add a function to FX.25 draft.
One large FX.25 frame by combining multiple blocks.
Long packet can be sent in a single frame of FX.25 without splitting it up.
Any higher level protocols can use the FEC with relative ease.
More resistant to further burst errors.
Compatibility with the existing AX.25 facilities is maintained.
Notes: Long AX.25 packet can be sent in a single frame of FX.25 without splitting it up.
That will be easier to operate and implement the system using error correction communication using the existing environments.
This means that not only AX.25 but also various higher level protocols can use the error correction function with relative ease.
It is possible the system to be more resistant to further burst errors as the effect of constructing a frame with multiple blocks.
Compatibility with the existing AX.25 facilities is maintained.

## Slide 15
Correlation Tag
RS Message
RS Parity
One RS block (255bytes)
If you want to fix N bytes error in a block,
the message size will be up to 255-2N bytes.
Frame structure of FX.25 drafts:
Correlation Tag
RS Message
RS Parity
One RS block (255bytes)
Notes: Frame structure of FX.25 drafts:
In the FX.25 draft, if the data did not fit in the RS block, the data was split and sent as multiple FX.25 frames.

## Slide 16
Correlation Tag
RS Message
RS Parity
RS Message (255-2N bytes)
Flag
Addresses
Control /PID
AX.25 packet frame
Information
FCS
Flag
Bit stuffing range
2 bytes
Up to 17 bytes
Flag
Addresses
Control /PID
Information
FCS
Flag
Complete bit pattern
when transmitting
AX.25
Up to 256 bytes
Up to 332 bytes?
Umm. I cannot stuff to The Packet.
FX.25 packet frame
Notes: The maximum I field length in AX.25 ver.1 is 256 bytes. This packet may have more than 300 bytes due to bit stuffing, AX.25 header and FCS. Therefore, this packet cannot be sent in a single FX.25 frame, so the frame is fragmented.

## Slide 17
Flag
Addresses
Control /PID
Information
FCS
Flag
Need to re-framing :
Flag
Addresses
Control /PID
Information
FCS
Flag
Flag
Addresses
Control /PID
Information
FCS
Flag
Correlation Tag
RS Parity
Correlation Tag
RS Parity
AX25
FX25
Data increased by packet division
Notes: FX.25 TNC side needs to have re-framing feature for AX.25. And, the FX.25 frame is added more bytes of Correlation Tag, flags, address fields, control fields, FCS, pads, etc.
This constraint causes a decrease in transmission efficiency.

## Slide 18
The position of FX.25 in the OSI protocol layers
Layer1 Physical Layer
AX.25
Layer3 & up Network Layer &
other
Layer2 Data Link Layer
Segment/Reassemble
AX.25 Layer3/ NETROM/ TCPIP etc.
Link & Address control
Bit stuff/Unstuff
Flag handle
Flame check
Forward error correction
FEC SYNC
Frame synchronization
NRZI
1200bps
AFSK
Scramble
9600bps
GFSK
Radio
Bit sync
Bit sync
FX.25
not clearly separated
Notes: And ,the lower protocol must know the frame structure of the higher protocol, which adds overhead between protocols and loses protocol independence.

## Slide 19: Solution: One large FX.25 frame by combining multiple blocks.
It enables FX.25 to send long messages.
You don't need to split the frame.
The problems presented in the previous section will be solved.
Notes: One large FX.25 frame by combining multiple blocks. It enables FX.25 to send long messages.
You don't need to split the frame.
The problems presented in the previous section will be solved.

## Slide 20: Multiple RS blocks in one FX.25 frame
RS
message
RS parity
Correlation Tag
RS
Message 1
RS parity 1
RS
Message 2
RS parity 2
If we simply put the blocks in order…
In this case, the message is divided by parity, and the packet cannot
be sent in a way that can be decoded by the existing AX.25 TNC
without any overhead.
Correlation Tag
Correlation Tag
RS
Message 2
RS parity 2
NG
Notes: Now consider the use of multiple RS blocks in a single frame.
If the RS blocks are arranged in the order of message and parity, the messages are divided by the parity and the code cannot be received by the existing facilities.

## Slide 21: Maintaining AX.25 compatibility in multiple block frames
not divided
Arrange the message parts so
that they are contiguous.
Messages are not divided by parity. Packets whose message length
exceeds the original RS message length can be sent without splitting.
RS
Message 1
RS parity 1
RS
Message 2
RS parity 2
Correlation Tag
RS
Message 1
RS parity 1
RS
Message 2
RS parity 2
Correlation Tag
OK
Correlation Tag
Notes: Therefore we arrange multiple blocks of messages together and then place the multiple parities behind messages.
Since the message part is continuous we can keep compatibility with the existing facilities.
The upper protocol is not limited to AX.25 because the data from the upper layer can be sent without processing that part.

## Slide 22: Interleaving
RS
Message 1
RS
Parity 1
RS
Message 2
RS
Parity 2
Correction Tag
By interleaving :
1. Improved burst error resistance.
2. Ensuring continuity of the message part in a form that is easy to process by software.
Message part
Parity part
RS encode
RS encode
Notes: Also, here, interleaving can be introduced to increase burst error resistance.
Interleave and parity calculation are performed while maintaining the AX.25 packet structure.

## Slide 23: Correlation Tag Exhaustion by Expansion
We propose a format that combines two types of Correlation Tags for frame with multiple blocks to reduce the number of Tags consumed in the future.
Notes: We propose a format that combines two types of Correlation Tags for frame with multiple blocks to reduce the number of Tags consumed in the future.

## Slide 24: FX.25 Correlation Tag Code (part1)
Tag | Correlation Tag Value | Encoding Type | Tag type
00 | 0x566ED2717946107E | Reserved | 
01 | 0xB74DB7DF8A532F3E | RS(255,239) | Tag-1
02 | 0x26FF60A600CC8FDE | RS(144,128) | Tag-1
03 | 0xC7DC0508F3D9B09E | RS(80,64) | Tag-1
04 | 0x8F056EB4369660EE | RS(48,32) | Tag-1
05 | 0x6E260B1AC5835FAE | RS(255,223) | Tag-1
06 | 0xFF94DC634F1CFF4E | RS(160,128) | Tag-1
07 | 0x1EB7B9CDBC09C00E | RS(96,64) | Tag-1
08 | 0xDBF869BD2DBB1776 | RS(64,32) | Tag-1
09 | 0x3ADB0C13DEAE2836 | RS(255,191) | Tag-1
0A | 0xAB69DB6A543188D6 | RS(192,128) | Tag-1
0B | 0x4A4ABEC4A724B796 | RS(128,64) | Tag-1
0C | 0x0293D578626B67E6 | 2 x RS(255,239) | Tag-1
0D | 0x41C246CB5DE62A7E | 2 x RS(255,223) | Tag-1
0E | 0x720267AF1BE1F846 | 2 x RS(255,191) | Tag-1
0F | 0x93210201E8F4C706 | 3 x RS(255,191) | Tag-1
continued |  |  | 
Notes: The Correlation Tag specified in FX.25 draft standard has the function of specifying frame synchronization, frame length, and coding scheme in one Tag. A large number of Tags would be required if we allocating Correlation Tag in an exhaustive manner with respect to the combination of block length and coding scheme. 64 of FX.25-defined Gold code sequence PN codes would be easily exhausted as a result.

## Slide 25: Frame length expansion format with 2nd Tag
RS
Message part
(Several messages)
Correlation Tag-1
Correlation Tag-2
RS parity part
(Several parities)
Frame length
The first tag specifies the length of the frame.
The second tag specifies the FEC coding algorithm.
Notes: How to reduce the number of new Correlation Tag allocations. The assignment method here defines a tag that represents the frame length. Separately, define and combine tags that represent the encoding within the frame. The first tag also provides frame synchronization capabilities. Although the headers look be larger the proposed method requires less data in total than the original multiblock structure in FX.25 draft standard.

## Slide 26: FX.25 Correlation Tag Code (part2)
Tag | Correlation Tag Value | Encoding Type | Tag type
10 | 0x10A58F97533893FA | Reserved | 
11 | 0xF186EA39A02DACBA | Reserved | 
12 | 0x60343D402AB20C5A | 2 x Specified by PN2 | Tag-2 (with Tag-3)
13 | 0x811758EED9A7331A | 3 x Specified by PN2 | Tag-2 (with Tag-3)
14 | 0xC9CE33521CE8E36A | 4 x Specified by PN2 | Tag-2 (with Tag-3)
15 | 0x28ED56FCEFFDDC2A | 5 x Specified by PN2 | Tag-2 (with Tag-3)
16 | 0xB95F818565627CCA | 6 x Specified by PN2 | Tag-2 (with Tag-3)
17 | 0x587CE42B9677438A | 7 x Specified by PN2 | Tag-2 (with Tag-3)
18 | 0x9D33345B07C594F2 | 8 x Specified by PN2 | Tag-2 (with Tag-3)
19 | 0x7C1051F5F4D0ABB2 | 9 x Specified by PN2 | Tag-2 (with Tag-3)
1A | 0xEDA2868C7E4F0B52 | 10 x Specified by PN2 | Tag-2 (with Tag-3)
1B | 0x0C81E3228D5A3412 | 11 x Specified by PN2 | Tag-2 (with Tag-3)
1C | 0x4458889E4815E462 | 12 x Specified by PN2 | Tag-2 (with Tag-3)
1D | 0xA57BED30BB00DB22 | 13 x Specified by PN2 | Tag-2 (with Tag-3)
1E | 0x34C93A49319F7BC2 | 14 x Specified by PN2 | Tag-2 (with Tag-3)
1F | 0xD5EA5FE7C28A4482 | 15 x Specified by PN2 | Tag-2 (with Tag-3)
continued |  |  | 
Table.2
Notes: This allocation method enables large-scale expansion to support arbitrary frame lengths, numerous encoding methods, new protocols.

## Slide 27: FX.25 Correlation Tag Code (part3)
Tag | Correlation Tag Value | Encoding Type | Tag type
20 | 0x9428192C9F6C6EFC | Use PN2 (Extended tag) | Tag-3 (show table A)
21 | 0x750B7C826C7951BC | Undefined | 
22 | 0xE4B9ABFBE6E6F15C | Undefined | 
23 | 0x059ACE5515F3CE1C | Undefined | 
24 | 0x4D43A5E9D0BC1E6C | Undefined | 
25 | 0xAC60C04723A9212C | Undefined | 
26 | 0x3DD2173EA93681CC | Undefined | 
27 | 0xDCF172905A23BE8C | Undefined | 
28 | 0x19BEA2E0CB9169F4 | Undefined | 
29 | 0xF89DC74E388456B4 | Undefined | 
2A | 0x692F1037B21BF654 | Undefined | 
2B | 0x880C7599410EC914 | Undefined | 
2C | 0xC0D51E2584411964 | Undefined | 
2D | 0x21F67B8B77542624 | Undefined | 
2E | 0xB044ACF2FDCB86C4 | Undefined | 
2F | 0x5167C95C0EDEB984 | Undefined | 
continued |  |  | 
Table.3
Notes: Tag No.20 is used as an extension tag. This ensures that the extension tag does not interfere with normal tags.

## Slide 28: FX.25 Extended Correlation Tag Code
Tag | Correlation Tag Value | Encoding Type | Tag type
20-0 | 0x9428192C9F6C6EFC | Reserved | Tag-3
20-1 (1bit rotated) | 0x4A140C964FB6377E | RS(255, 239) | Tag-3
20-2 (2bit rotated) | 0xA50A064B27DB1BBE | RS(255, 223) | Tag-3
20-3 (3bit) | 0xD285032593ED8DDE | RS(255, 191) | Tag-3
20-4 | 0xE9428192C9F6C6EE | Reserved | Tag-3
20-5 | 0xF4A140C964FB6376 | Reserved | Tag-3
20-6 | 0xFA50A064B27DB1BA | Reserved | Tag-3
20-7 | 0xFD285032593ED8DC | Reserved | Tag-3
20-8 | 0x7E9428192C9F6C6E | Reserved | Tag-3
20-9 | 0xBF4A140C964FB636 | Etc. | Tag-3
20-10 | 0xDFA50A064B27DB1A | Etc. | Tag-3
20-11 | 0xEFD285032593ED8C | Etc. | Tag-3
20-12 | 0x77E9428192C9F6C6 | Etc. | Tag-3
20-13 | 0xBBF4A140C964FB62 | Etc. | Tag-3
20-14 | 0xDDFA50A064B27DB0 | Etc. | Tag-3
20-15 to 20-62 |  |  | Tag-3
Table.A
Notes: Since the extended tag does not need the frame synchronization function, it is possible to use a bit-rotated version of the extended tag pattern already assigned. 63 tags can be assigned in this table space.

## Slide 29: FX.25 Correlation Tag Code (part4)
Tag | Correlation Tag Value | Encoding Type | Tag type
30 | 0xD2E344CAB512ED78 | Undefined | 
31 | 0x33C021644607D238 | Undefined | 
32 | 0xA272F61DCC9872D8 | Undefined | 
33 | 0x435193B33F8D4D98 | Undefined | 
34 | 0x0B88F80FFAC29DE8 | Undefined | 
35 | 0xEAAB9DA109D7A2A8 | Undefined | 
36 | 0x7B194AD883480248 | Undefined | 
37 | 0x9A3A2F76705D3D08 | Undefined | 
38 | 0x5F75FF06E1EFEA70 | Undefined | 
39 | 0xBE569AA812FAD530 | Undefined | 
3A | 0x2FE44DD1986575D0 | Undefined | 
3B | 0xCEC7287F6B704A90 | Undefined | 
3C | 0x861E43C3AE3F9AE0 | Undefined | 
3D | 0x673D266D5D2AA5A0 | Undefined | 
3E | 0xF68FF114D7B50540 | Undefined | 
3F | 0x17AC94BA24A03A00 | Undefined | 
40 | 0x41C246CB5DE62A7E | Reserved | 
Table.4
Notes: This extension creates a lot of space for correlation code allocation. We reserved a 16 x 63 tag space using the expansion tag. Almost half the allocation space is still free.

## Slide 30
Please visit PRUG website for further information.
http://www.prug.com/
Notes: Please visit PRUG web site for further information like schematics and software.
Sorry, most information on the site is in Japanese.
But recently Google translate works well often.
We welcome translation volunteers.